The ILP uses the following important variables:
X_i_s,X_i_e i€[1,n] X€[1,n-1?], the position of the respective start and end pockets
p	, the pathwidth of the decomposition
I_i_X_k i€[0,n-2] k€[0,n-1]	, indicator whether X_k is in the pocket at position i

ENTER var ranges seperated

As already discussed, in a valid path decomposition for each two pockets in which a node appears, it also has to appear in each node inbetween. The choice of representing the decomposition basically as list of start and endpoints of intervals already encapsulates this property in combination with the following condition 1:

1) X_i_s<=X_i_e Ai

With the guarantee that the intervals have a valid format, a large part of the conditions required for a valid path decompostion are already fullfilled. The only requirement left is to ensure that in the case of two connected nodes they at least once appear together in a pocket. This is equivalent to the overlap of the intervals X_I and X _J ANDERER TEXT .This is achieved by conditions 2 and 3:
2) X_i_e >= X_j_s if (i,j)€E
3) X_j_e >= X_i_s if (i,j)€E

That the fullfillment of the condition automatically leads to the overlap of the intervals, given that the interval limits are properly defined, i.e., that the beginning of the intervals lies before its end, can best be seen by the following diagram:

DIAGRAMM

#With this alone, each variable assignment fullfilling 1) and 2) would be a valid decompostion. What remains to be done is to define the value to be minimized, i.e., the pathwidth.